## Slide 1: Embedded Bluetooth Stack
Dean Camera
Project Supervisor: John Devlin

## Slide 2: Overview
Design and implement an embedded Bluetooth Stack
Create a simple test robot to demonstrate its use
  Sensors
  Motors
Control robot with consumer Bluetooth devices
  Mobile phone for movement
  Computer to read and log sensor data

## Slide 3: Bluetooth
Simple wireless communication technology
  Phones
  Headsets
  Computers
Short Range
  Unregulated frequency band
  Three power levels (classes)

## Slide 4: Bluetooth (Cont.)
Keys to success:
  Universal compatibility
  Custom class support
  Low Power
Various standardized classes and services
  SDP
  HID
  RFCOMM
  Etc.

## Slide 5: Existing Stacks
Free implementations
  Linux, BSD, Solaris, etc.
Advantages:
  Ready for immediate integration
  Large number of standard classes supported
Disadvantages:
  Designed for desktop use only
  Large, complex, written for devices with MMU

## Slide 6: Embedded Bluetooth Stacks
Very few existing embedded stacks
Almost exclusively designed for embedded OS use
Expensive
  “Contact Us” pricing model
Restricted Use
  Binary Only
  Source Code

## Slide 7: Previous Work
The LUFA Software Stack
  Handles USB layer to the Bluetooth adapter
Proof of concept Bluetooth Stack
  Basic functionality
  Architectural issues

## Slide 8: System Block Diagram
Sensor Boards
Level Translator
PWM Controller
Motors
AVR Microcontroller
USB Bluetooth Adapter
LCD, Speaker, LEDs and Buttons
3.3V Supply
5V Supply
9V Battery

## Slide 9: Hardware
Premade robot base
  6V DC motors
  Gears and tank tread assembly
AA Battery pack
  May replace with Li-ion at later stage

## Slide 10: Hardware (Cont.)
Micropendous-3 Control Board
  Atmel AT90USB647 Microcontroller
    64KB FLASH, 4KB SRAM, 2KB EEPROM
    16MHz Crystal for approximately 16 MIPS
  USB Connector for USB Bluetooth Module
  128KB External SRAM (Packet Buffer)
Speaker, Buttons, LEDs, LCD Display
H-Bridge for dual PWM motor control

## Slide 11: Hardware (Cont.)
Level translated I2C Bus for sensor boards
Atmel INERTIAL ONE sensor board
  Temperature
  Magnetometer
  Accelerometer
  Gyroscope
Atmel PRESSURE ONE sensor board
  Air Pressure

## Slide 12: Firmware
LUFA for low level USB transport
Stack to be written in the C language
Emphasis on:
  Low resource usage
  No embedded OS requirement
  Ability to integrate into existing applications

## Slide 13: Firmware (Cont.)
Bluetooth stack layers to implement:
Physical Transport
Host Controller Interface
Logical Link Control
and Adaption Protocol
HID
SDP
RFCOMM
Sends/Receives packets to and from the Bluetooth Controller
  USB
  Serial
Low level connections between devices
Logical channel management within a device connection
Manages service discovery and negotiation between devices
Implements human interface functions such as keyboards and mice
Implements RF communications such as Virtual Serial Ports
Complete Stack

## Slide 14: Work Completed
Schematic Designed
Board Layout Completed
Parts Ordered
PCB Ordered and Received
Second board revision ready for manufacture
Coding ready to begin

## Slide 15
Schematic Design
PCB Layout
Construction
Coding
Testing
Timeline
Semester 1
Semester 2
Completed
In Progress
Not Started

## Slide 16
Thank you for your attention
Questions?