## Slide 1
Dean Camera
Supervisor: Prof. John Devlin
Co-Supervisor: Robert Ross
Embedded Bluetooth Stack

## Slide 2: Project Aims
Develop a functional Bluetooth stack
  Designed for embedded use
  Focus on low resource usage
    Memory Requirements
    CPU Requirements
  No RTOS requirements
Design and build a functional hardware prototype to demonstrate the stack

## Slide 3: Bluetooth Stack

## Slide 4: Bluetooth Stack Layers
Physical Transport
Host Controller Interface
Logical Link Control
and Adaption Protocol
Other Services
SDP
Sends/Receives packets to and from the Bluetooth Controller
  USB
  Serial
Baseband management including physical connections between devices
Logical channel management within a device connection
High level abstracted services

## Slide 5: Completed Bluetooth Stack
Supports multiple concurrent connections
Multiple logical channels per connection
L2CAP reliability through a dedicated internal queue
API for integration into user applications

## Slide 6: Bluetooth Services
RF Communication (RFCOMM)
  Server role only
  Provides wireless serial port functionality
Human Interface Device (HID)
  Very basic server implementation
  Compatible with specific devices only

## Slide 7: Completed Services (Cont)
Service Discovery Protocol (SDP)
  Server implementation only
  Allows for dynamic registration of other services

## Slide 8: Demonstration Hardware

## Slide 9: Hardware Overview
Small battery operated “ExplorerBot” robot
Allow for user control over Bluetooth connections
Onboard sensors with wireless streaming

## Slide 10: Hardware Overview (Cont)
Atmel Inertial One and Pressure One sensor boards
  Accelerometer
  Gyroscope
  Magnetometer
  Temperature Sensor
  Pressure Sensor
Level Converted I2C Bus

## Slide 11: Completed Prototype

## Slide 12: Firmware Block Diagram

## Slide 13: Tested Bluetooth Devices
Motors, horn and headlights controllable
  Sony Ericson z550i Mobile Phone
  Sony Playstation 3 Controller
  Nintendo Wii Controller

## Slide 14: Host Application
Basic sensor streaming host application
  Written in C#
  Graphs sensor data from the robot in real time

## Slide 15: More Information
All project materials (source code, thesis, presentations, photos) uploaded online
Source code released under a MIT license
Full SVN revision history available
www.fourwalledcubicle.com/ExplorerBot.php

## Slide 16
Thank You
Notes: This is the “back slide” in your presentation to show that you have completed your presentation.